## Slide 1: Scalable 5-Tuple Packet Classification in Overlay Network
Muhammad Arif
September 7, 2016
Notes: Hello Good Morning
Thanks for coming
Today I will present about my thesis work with title

## Slide 2: Agenda
Introduction
  Background
  Problem Statement
  Platforms Overview
Development
  5-Tuple LCAF & Mapping System
  Rule Aggregation
  Flow Classification
Result & Analysis
Conclusion and Future Works

## Slide 3: Introduction

## Slide 4: Introduction
Traditional Networking
Destination-based Forwarding
No global view, multiple control plane
Problems: Number of rules increases and rule size increases
  processing latency increases
  storage space requirement also increases
OpenFlow
Up to 38 packet header fields
(SDN) Has global view, centralized control plane
Notes: Kasi panah

## Slide 5: Problem Statement
Trade-off between flexibility vs performance: 5-tuple
Objectives:
  Propose rule aggregation algorithm to minimize number of entries stored  reduce the storage space requirement
  Propose flow classification method to minimize the lookup time  reduce processing latency
Flexibility
Performance
SDN
TN
5-Tuple
Notes: Kasi gambar 5-tuple

## Slide 6: Related Works
Packet Classification: Well-known topic for research
Decision-tree based:
  Well-known approach, such as in HiCut and HyperCut
  Cons: Tree size grows significantly due to finer TE
TCAM-based:
  Fast lookup process
  Cons: high implementation cost
Tuple Space Search (TSS):
  Very flexible
  Cons: high processing latency for high number of rules
Main Idea: MC-SBC
  Modified TSS
  Send rules and packets to specific smaller lookup tables
Notes: TCAM: Specialized memory for fast lookup
MC-SBC: multidimensional-cutting via selective bit-concatenation

## Slide 7: Platform Overview

## Slide 8: Open Overlay Router (OOR)
Overlay network is one of the well-known implementation of SDN
OOR: Open-source platform to create programmable overlay network

## Slide 9: Vector Packet Processing (VPP)
High performance packet processing platform and runs entirely in the userspace
Process multiple packets in a time by building superframe
Packets are processed through Packet Processing Graph

## Slide 10: VPP Classifier
Using mask-and-match model
Two main parts: Tables and Sessions
Notes: Salah iP

## Slide 11: Developments

## Slide 12: 5-Tuple LCAF Implementation
2-Tuple LCAF (Current)
5-Tuple LCAF
Based on RFC Draft:
LISP support for Multi-Tuple EIDs

## Slide 13: 5-Tuple Mapping System
Goals:
  Faster Lookup Times
  Reduce amount of Control Message
Three Layers of Information Bases:
  NIB: Whole TE Rules
  RIB: Subset of NIB
  FIB: Ready-to-use Info

## Slide 14: 5-Tuple Mapping System (Cont.)
Structure:
  Key: 5-Tuple Information
  Match: Destination RLOC and Action
  Tag: Copied/Not-Copied to next database (NIBRIBFIB)
    To be used during update/removal of rules

## Slide 15: Rule Aggregation and Flow Classification
Developed based on VPP Classification method
Basic Ideas:
  Splitting rules into each header fields
  Limiting wildcard positions during aggregation
  Using Multiple Tables for classification

## Slide 16: Rule Aggregation
VPP classifier does not accept variable-sized header (wildcards) mask
Goals:
  Minimize the number of entries
  Give flexibility to use wildcards (predicted)
Predicted vs Free Wildcard Positions (4 bits rules)
Predicted | Free Wildcard Positions |  |  | 
1111 | 1111 | 0111 | 1010 | 0010
0111 | 1110 | 1100 | 0101 | 0100
0011 | 1101 | 1001 | 0110 | 1000
0001 | 1011 | 0011 | 0001 | 

## Slide 17: Rule Aggregation (Cont.)
Inserted rules (with wildcards) are broken down into multiple entries to remove the wildcards
The entries are converted into binary and split into each packet header fields and inserted to matrix
Matrix is inserted into the the rule aggregation algorithm and results in aggregated rules matrix

## Slide 18: Rule Aggregation (Cont.)

## Slide 19: Rule Aggregation (Cont.)
Fields | Value | Binary* | Size
SRC Addr | 172.205.10.1 | {0,0,0,1} | 32 bits
DST Addr | 245.206.13.2 | {0,0,1,0} | 32 bits
SRC Port | 80 | {0,0,0,0} | 16 bits
DST Port | 20-24 | {0,1,0,0} {0,1,0,1} {0,1,1,0} {0,1,1,1} {1,0,0,0} | 16 bits
Protocol | TCP (6) | {0,1,1,0} | 8 bits
Notes: Sikat semua

## Slide 20: Rule Aggregation (Cont.)
Fields | Value | Binary* | Size
SRC Addr | 172.205.10.1 | {0,0,0,1} | 32 bits
DST Addr | 245.206.13.2 | {0,0,1,0} | 32 bits
SRC Port | 80 | {0,0,0,0} | 16 bits
DST Port | 20-24 | {0,1,0,0} {0,1,0,1} {0,1,1,0} {0,1,1,1} {1,0,0,0} | 16 bits
Protocol | TCP (6) | {0,1,1,0} | 8 bits
Notes: Sikat semua

## Slide 21: Flow Classification
Goal: reduce the lookup times
Similar to Tuple Space Search method, but based on specific bit position
Process: Offline and Online Stages
Pre-filtering: select one or more bit positions to split the rules into smaller multiple lookup tables as even as possible

## Slide 22: Flow Classification (Cont.)
Bit positions selected for the pre-filtering  Effective Bit Position (EBP)
To determine EBP:
  Diversity Index: to find most even distribution of zeros and ones
  Independence Index (for >1 EBP): to find bit positions that draws good distinction between entries

## Slide 23: Flow Classification (Cont.)
Best case scenario: High and
EBP has to be updated periodically, especially if there’s many rules addition
In the beginning, when there’s no rules (day 0): select EBP at random

## Slide 24: Flow Classification (Cont.)
Entries | SRC Addr | DST Addr | SRC Port | DST Port | Protocol | Action
 | 00011 | 0001* | ***** | 101** | 00110 | action1
 | 00011 | 00100 | ***** | 101** | 00110 | action1
 | 00101 | 00010 | ***** | 10110 | 10001 | action2
 | 00110 | 00010 | ***** | 10110 | 10001 | action2
 | 00111 | 0000* | ***** | 101** | ***** | action3
Entries | SRC Addr | DST Addr | SRC Port | DST Port | Protocol | Action
 | 00011 | 0001* | ***** | 101** | 00110 | action1
 | 00011 | 00100 | ***** | 101** | 00110 | action1
 | 00101 | 00010 | ***** | 10110 | 10001 | action2
 | 00110 | 00010 | ***** | 10110 | 10001 | action2
 | 00111 | 0000* | ***** | 101** | ***** | action3
Offline Stage

## Slide 25: Flow Classification (Cont.)
Entries | SRC Addr | DST Addr | SRC Port | DST Port | Protocol | Action
 | 00011 | 0001* | ***** | 101** | 00110 | action1
 | 00011 | 00100 | ***** | 101** | 00110 | action1
 | 00101 | 00010 | ***** | 10110 | 10001 | action2
 | 00110 | 00010 | ***** | 10110 | 10001 | action2
 | 00111 | 0000* | ***** | 101** | ***** | action3
Entries | SRC Addr | DST Addr | SRC Port | DST Port | Protocol | Action
 | 00011 | 0001* | ***** | 101** | 00110 | action1
 | 00011 | 00100 | ***** | 101** | 00110 | action1
 | 00101 | 00010 | ***** | 10110 | 10001 | action2
 | 00110 | 00010 | ***** | 10110 | 10001 | action2
 | 00111 | 0000* | ***** | 101** | ***** | action3
Online Stage

## Slide 26: Implementation in VPP
Offline Stage

## Slide 27: Implementation in VPP (Cont.)
Online Stage

## Slide 28: Results & Analysis

## Slide 29: Simulation and Testing Setup
Testbed using VMs to implement OOR and VPP
Synthetic rules generator: Classbench
Packet generation: hping3
Name | Function
VM1 | VPP and Classbench
VM2 & VM3 | xTR and hping3
VM4 | MS and hping3

## Slide 30: Result: Rule Aggregation
Number of stored entries can be reduced
Minimum achievable aggregation: 41.4%
Higher number of original rules lead to more aggregation
Original | Aggregated | %
1607 | 1419 | 94.5
8640 | 6573 | 76.0
31571 | 16357 | 51.8
74527 | 31321 | 42.02
84815 | 35367 | 41.7

## Slide 31: Result: Flow Classification
Lookup times can be reduced
After 76 entries, the performance of proposed method surpassed the basic method
Maximum achievable reduction: 29.6%

## Slide 32: Conclusions

## Slide 33: Conclusions
SDN provides flexibility and programmability, but it comes with scalability problem
Implementation of proposed 5-tuple rule aggregation and flow classification are able to reduce:
  Number of entries stored  less storage space requirement
  Lookup times  lower processing latency
In the testing phase, we found:
  58.6% savings in storage space requirement
  29.6% reduction in processing latency

## Slide 34: Future Works
Extend the proposed rule aggregation
  To check for overlapping rules
  To find faster way for calculation
Extend the flow classification method
  Calculate and Update EBP in real time
  Other method to determine EBP
To check the effectiveness of the proposed methods in the real and big network

## Slide 35: Thank You!

## Slide 36: Introduction
Traditional networking: destination-based forwarding
  Only consider single header field  scalable but not flexible
  No global view of the network  programmability problem for complex TE rules
Software-Defined Networking:
  Flexible  up to 38 packet header fields can be observed
  Has global view of the network  centralized control plane  easy to program
Problem: requirement for more specific traffic engineering rules  rule size increases
  processing latency increases
  storage space requirement also increases

## Slide 37: Result: Flow Classification
Number of entries to be checked can be minimized
In average only 56.9% of entries that needs to be checked
Reason: multiple lookup tables